Future Impact software updates

Software update numbering:

If both software are updated at the same time, they get an equal number that is higher than the last version of either. In this case maybe (but not necessary) that both are not compatible with previous versions. 
If one of them is updated independently of the other then it should get a number that is higher than either. This case means of course, there may not be any change of compatibility. 

If both would be numbered just sequentially, independent of each other then you may know that you have to use the highest version of both to be compatible, but if for any reason you have to get back to an older one then you are lost. With this scheme e.g. if for any reason you must use an older version of the FI, then you know that you have to use the editor with the same number, or if it does not exist then the highest smaller number.

Date:			FI device software:		FI editor software:

03/06/2016		1.01				1.01

04/28/2016		1.22				1.22

09/19/2016						1.23

09/25/2016		1.30

12/07/2016		1.31

12/11/2016		1.32

06/24/2017		1.33

11/06/2017		2.03

FI device software history:

1.01:

1.) Bugfix: The Edit/Bank Up wheel was prelling on some devices. Prell suppression software enhanced.

2.) Bugfix: Detent position 10 (“LEVEL”) was slightly shifted on most devices. Moved higher.

3.) Bugfix: MIDI channel of the default programs 46 and 54 were not OMNI. Set to OMNI, just like in all other programs.

1.22:

1.) Effect on-off control through MIDI: Control 66 (Sostenuto) is used for this. If <64 then switch the relay to bypass, if >=64 then to effect.

2.) Program decrement switch: Control 67 (Soft pedal) is used for this. If >=64 then first it makes one step down, then it starts to scroll, just like the Program Up does. Stops if <64.

3.) Global Parameters: Up to this version the FI had two global parameters, Reset and Program Mode. This will be enhanced, and editing is changed a little bit in order to have a better overview. Programming Global Parameters: Boot FI with Program footswitch pressed, and then turn the Parameter selector to the leftmost position, Note Off Level. In this case the display will show the abbreviation of the Global Parameter Name. You can step through the parameters by pressing the Program Footswitch, it scrolls around these Parameters. When you selected the Parameter that you want to change, you can turn the Parameter Selector to any of the higher positions. In this case the display changes to the Global Parameter Value. When you selected Value, you can edit it with the data wheel. When a parameter was edited, it will be immediately stored in the memory. The parameters are:

Parameter:					Value:

rS: Reset					0,1: 1=perform reset

PrG: Program Mode				0: DEFAULT, 1: DIRECT

GLb: Global MIDI Channel		All (for OMNI), 1,2,3,…16

vCF: VCF control (74) range adjust	1:+-1 oct., 2:+-2 oct., 4:+-4 octaves

The Global MIDI Channel is replacing the MIDI channel setting in the FI programs that were used until this version. The MIDI Channel setting is active for both MIDI input and for output (sending Program Change). If OMNI mode is selected then the MIDI output channel for Program Change that is sent out will be channel 1.

4.) Breath controller: The breath controller (2) adjusts the VCF volume of the Output Mixer in the same way as the LFO modulations work: when the MIDI breath controller is at maximum (127) then this corresponds to the preset value in the program. This differs from Volume Control (7) in two aspects:

a.) it adjusts only the synth voice volume, does not change the bass;

b.) it is before the effects, so delay effects will not be muted out when this controller is pulled down.

5.) MIDI THRU: Passing all information from the MIDI input to the output, except Ctrl 6 (Data Edit), NRPN controllers and System Exclusive data.

6.) Program Change Out: Whenever a program change happens on the FI, it sends out the appropriate Program Change command on the MIDI OUT on the effective MIDI Channel, if it was caused by pressing the Program pedal, or a Program Decrement command on the MIDI IN, but not by a Program Change on MIDI IN (this will appear on MIDI OUT anyway, due to THRU).

7.) Bugfix: When parameter edit is aborted by the ON/OFF or the PROGRAM footswitch, it should return to the original display.

8.) Bugfix: EQ Mid and Bass parameter ranges slightly changed in order to avoid faulty conditions.

9.) Global parameter editing through System Exclusive from computer.

1.30:

1.) Factory calibration of parameter scale. No features affecting users.

1.31:

1.) Bugfix in test mode. No features affecting users.

1.32:

1.) Accent parameter implemented (on place of MIDI channel, will require editor change).

1.33:

1.) Encoder contacts reversed for better prell suppression. No features affecting users.

2.03:

1.) Tuner. Press and hold ON/OFF for a second. In either case if it was ON or OFF, it will go ON, but the output will be muted (audibly it will go off). Tuner is activated. The first digit shows the note, the second the # sign, and the third the fine tune value with one or more of the three horizontal lines. The lower line alone means flat by > 10 cents, lower and middle flat by > 3 cents, the center line means OK (within +-3cents), middle and upper line sharp by > 3 cents, upper line sharp by > 10 cents. Press ON/OFF briefly, and it returns to ON state. While in tune mode, the display is blank if there is no signal.

2.) Passing sys real messages. Some users complained that while MIDI channel messages are passed through, sys real messages, especially timing clock does not. This is corrected now, timing clock, start, continue, stop is passed as well.