Future Impact new features

Version 2.03

- Tuner. Press and hold ON/OFF for a second. In either case if it was ON or OFF, it will go ON, but the output will be muted (audibly it will go off). Tuner is activated. The first digit shows the note, the second the # sign, and the third the fine tune value with one or more of the three horizontal lines. The lower line alone means flat by > 10 cents, lower and middle flat by > 3 cents, the center line means OK (within +-3cents), middle and upper line sharp by > 3 cents, upper line sharp by > 10 cents. Press ON/OFF briefly, and it returns to ON state. While in tune mode, the display is blank if there is no signal.

- Passing sys real messages. Some users complained that while MIDI channel messages are passed through, sys real messages, especially timing clock does not. This is corrected now, timing clock, start, continue, stop is passed as well.